Recognized verbal instructions for 手元TEMOTO teleoperator

“NAVIGATION” / Operator takes control of the robot base for navigation.	“MANIPULATION” / Operator takes control of the right manipulator.
“NATURAL CONTROL MODE” / Operator's hand and robot's base are considered to be oriented the same way. / “IGNORE ROTATION” / Hand rotation (orientation) is not transferred to robot's base, i.e. the current rotation of the base is maintained at goal position. / “CONSIDER ROTATION” / Hand rotation (orientation) will be considered when setting a target goal for the base.	“NATURAL CONTROL MODE” / Operator's hand and robot's end effector are considered to be oriented the same way. / “INVERTED CONTROL MODE” / Left and right are inverted for operator's hand and robot's end effector. / “IGNORE ROTATION” / Hand rotation (orientation) is not transferred to robot's end effector, i.e. the rotation of the end effector will not be altered. / “CONSIDER ROTATION” / Hand rotation (orientation) will be considered when setting a target pose for the end effector. / “LIMIT DIRECTIONS” / Only displacement in certain direction(s) is considered when setting a target pose for the end effector. / NOTE: Right hand switches between in-plane and forward constraints. / “FREE DIRECTIONS” / Displacement of the operator's hand in any direction will be considered when setting a target pose.
“ROBOT PLAN AND GO” / Robot will try to move to a goal specified by the hand marker.	“ROBOT PLEASE PLAN” / Start the planner for moving the end effector to the pose determined by operator's hand. / “ROBOT PLEASE EXECUTE” / Execute the latest plan available. / “ROBOT PLAN AND GO” / Start the planner and execute right after. Equivalent of Plan & Execute. / “ROBOT PLAN HOME” / Start the planner for returning to a saved home pose. / “ROBOT PLEASE GO HOME” / Plan and execute the return to the saved home pose.